## Slide 1: SoftHier Dequantization Meeting 25.08.25
Integrated Systems Laboratory (ETH Zürich)
Fatih Özdemir Bowen Wang
Yawei Li
Angelo Garofalo

## Slide 2: SoftHier Building Block
Core 0
Core 0
…
Core n
RedMule
iDMA
I $
TCDM (Multi-banked L1)
CTRL
REG
Interconnect
To Data NoC Router
To Sync NoC Router
TE Cluster
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
HBM
HBM
HBM
HBM
System Level
  Manycore NoC Architecture
  Each cluster has
    A Vector Processor
    L1 Memory (~1 MiB)
    Inter-Cluster Broadcast and Communication
2

## Slide 3: Vector Quantization
v
Vector v = [-0.5, -0.2]
Centroid1 = [-2 2]
Centroid2 = [2 -2]
Centroids stored in codebook
Codebook=[centroid1
centroid2]
Assign v to centroid 2
Encoded Index to access codebook entry [0-> centroid1
1-> centroid2]

## Slide 4: Dequantization
Look up the Encoded Index in the Codebook -> Indirect Access needed

## Slide 5: AQLM
Quantize the rows of a Matrix
Additive Quantization: Reconstructed Matrix is sum of M codewords from M codebooks
For B Bits Indices, we can access Entries in the Codebook

## Slide 6: AQLM Quantization
For a Big Matrix, It is also possible to split W by groups vertically along the columns and quantize each group g separately (with the same codebook)
-> Can Dequantize different columns with the same codebook simultaneously In Multicore Setting
-> Each centroid has size (1,g)
We still encode row by row

## Slide 7: AQLM Quantization
1) scale (divide by the scaled value
2) assign the to-be-encoded row to nearest centroid in both codebooks
3) store the nearest centroid location

## Slide 8: AQLM Quantization

## Slide 9: AQLM Dequantization
Each decoding step decodes g elements(size of centroid)
  Decompression happens along the rows

## Slide 10: AQLM Configs
Parameters to Quantize:
  M = Number of Codebooks
  g = Group Size
  B = Number of Indices Bits
  AQLM’s best results use
 | Codebook Size | Indices Shape | Memory Footprint (Codebook Size + Indices Size) | Bits per parameter
M=2,g=8,B=8 | [2,256,8] | [4096, 512] | 8 KiB+ 4 MiB~4 MiB | 2.01
M=1,g=8,B=16 | [1,65536,8] | [4096, 512] | 1 MiB+ 4 MiB=5MiB | 2.38

## Slide 11: AQLM Configs
Config 2 requires 1 MiB codebook Size which won’t fit into a single cluster
-> Config 1 with 2 codebooks and smaller codebook size is preferred

## Slide 12: VPTQ
Encode Columns of a Matrix
Reshape Weight Matrix -> many columns, few rows
Quantize each column separately and update weight matrix at each step
Quantize Column by Column (in Contrast, AQLM: row by row)

## Slide 13: VPTQ Dequantization

## Slide 14: VPTQ Configs
Parameters to Quantize:
  v = Size of Centroid
  K = Number of Centroids
  VPTQ’s best results use
 | Codebook Size | Indices Shape | Memory Footprint | Bits per parameter
V=6,K=4096 | [4096,6] | [683, 4096] | 48 KiB+ can4 MiB~4 MiB | ~2
V=6,K=4096 g=8 | [4096,6]*8 | [683, 512] | 48 KiB*8+4 MiB~4.4 MiB | ~2
V=8, K=32768 | [32768,8] | [4096, 512] | 0.5 MiB+ 4 MiB=4.5MiB | ~2

## Slide 15: Matrix Multiplication
Main Idea:
Fuse Dequantization and Multiplication to Avoid multiple Memory Accesses

## Slide 16: Benchmark VPTQ and AQLM
1) Benchmark Memory Footprint of Indices and Code Shapes(+Scales for AQLM)
2)Benchmark Reconstruction Error
Benchmarked Configs:
  AQLM: M=2,g=8,B=8(256 codebook entries)
  VPTQ: k=4096, v=6, No Product Quantization
  VPTQ: k=4096, v=6, Product Quantization: Split Matrix W by 8 vertically , each having their own codebook entries

## Slide 17: Benchmark Memory Footprint

## Slide 18: Benchmark1: Reconstruction Error

## Slide 19
Type equation here.

## Slide 20: Decisions
Deploy Dequantization with AQLM (M=2 codebooks,256 centroids,g=8 group size)
Implementing Dequantization + Inference on Spatz Vector Processor with existing RISC-V Vector Processor
Implement Basic GEMM Kernel in a single-cluster scenario
  Fully Materialized multiplied by a random Matrix to simulate an MLP Layer